## Slide 1: Work and Machines
Types of Machines

## Slide 2: Levers
Have you ever used the “claw” of a hammer to remove a nail?
If so, you were using the hammer as a lever.
A lever is a simple machine that has a bar that pivots at a fixed point, called a fulcrum.
There are 3 different classes of levers

## Slide 3: Levers
First-class levers
  The fulcrum is between the input force and the load
  They always change the direction of the input force
  Can be used to increase force or to increase distance

## Slide 5: Levers
Second-class levers
  The load is between the fulcrum and the input force
  The output force is greater than the input force

## Slide 7: Levers
Third-class levers
  The input force is between the fulcrum and the load
  Do not change the direction of the input force
  Do not increase the input force
  The output force is less than the input force

## Slide 9: Pulleys
Pulley- a simple machine that has a grooved wheel and holds a rope or a cable
  A load is attached to one end of the rope, and an input force is applied to the other end.
(input force)

## Slide 11: Wheel and axle
Wheel and axle- a simple machine consisting of two circular objects of different sizes
  Ex: doorknobs, wrenches, steering wheels

## Slide 12: Wheel and axle
Mechanical advantage of a wheel and axle
  Found by dividing the radius of the wheel by the radius of the axle
Example:
Radius of wheel is 15cm
Radius of axle is 3cm
MA= 15cm/3cm = 5
Since it’s greater than one, there is a mechanical advantage to this machine.

## Slide 13: Inclined Planes
Inclined plane- a simple machine that is a straight, slanted surface such as a ramp

## Slide 14: Inclined planes
Mechanical advantage
  The mechanical advantage of an inclined plane is the length of the inclined plane divided by the height to which the load is lifted

## Slide 15: Inclined planes
Mechanical advantage example:
  What is the mechanical advantage?
  Length divided by height
  6m / 3m
  2
6m
3m

## Slide 16: Wedges
wedge- a simple machine that is made up of two inclined planes and that moves; often for cutting
  Example: KNIFE

## Slide 17: Wedges
Mechanical advantage
  The longer and thinner the wedge is, the greater the mechanical advantage
    That’s why sharp knifes work better
  Mechanical advantage is length of wedge divided by the thickness

## Slide 18: Screws
Screw- a simple machine that consists of an inclined plane wrapped around a cylinder
  When a screw is turned, a small force is applied over the long distance along the inclined plane of the screw

## Slide 19: Compound machines
Compound machine- a machine made of more than one simple machines
Example: a can opener.
  Second-class lever when you squeeze the handle
  Wedge  blade of the can opener
  Wheel and axle  knob you turn to open the can

## Slide 20: Examples!
Levers
Pulleys
Wheel and axle
Inclined planes
Wedges
Compound machines
Notes: If time, have class come up with examples